BIA-AHS series

The pump is a submersible drainage pump fitted with semi vortex, eurethane coated impeller plus agitator, supplied wired and ready to install.

The pump has a dual mechanical seal in oil chamber and can handle particles to 25 mm x 10mm.

The pump is characterised by:

- Corrosion resistant pump components.

- Fully automatic operation.

- Dual Mechanical Seal in oil bath, SIC/SIC, Carbon Ceramic.

- Eurethane coated semi vortex impeller allows pumping of suspended solids, sandy and stringy material.

- Agitator on the end of the pump shaft helps prevent air locking and clogging.

- Carry handle.

- Versatile outlet connection.

- 240V single phase motor with in-built auto reset thermal overload.

      - 10m of power cable.

      - 12 months warranty.

      - Suitable for construction sites, storm water, basements.

Liquid:

Water temperature range:	2 – 35 deg C

Materials:

Pump body	Cast Iron

Strainer	Eurethane

Impeller	Eurethane coated semi vortex

Shaft		Stainless Steel 403

Shaft seal 	Dual Mechanical in oil bath, Silicon Carbide/Silicon Carbide + Carbon/Ceramic

Installation:

Maximum ambient temperature:	40 deg C

Maximum submergence 		8m.

Pipe connections discharge:		2”

Electrical data:

Rated voltage:		240V, 50Hz

Rated output		400, 750 W

Current:		2.8, 5.6 amps

Capacitor:		12, 20 uF

Motor duty:		Continuous

Motor protection:	In-built thermal overload,

Ingress protection:	IP 68

Insulation class:	F

Power cable length:	10 m	H07RNF

Net weight:		13.0, 15.5 kg

Dimensions:		240, 290 mm L x 330, 390 mm H x 190mm W

Pump Performance.		Flows to 220, 350 l/m

Heads to 12, 18 m

Maximum particle size 25 x 10 mm

# Text boxes

BIANCO SUBMERSIBLE PUMP

MODEL:	BIA-AHS05

BIA-AHS10

PRODUCT

## PROFILE